## Slide 1
Mechanical couplings and synchronous vibrations

## Slide 2
Single cardanic couplings
Vibrations in couplings are due to operation under misalignments, especially
Radial misalignment ( = parallel misalignment )
Angular misalignment
Angular misalignment
radial misalignment

## Slide 3
Single cardanic couplings
Typical for single cardanic drives is the increased amplitude
of the rotary frequency fn and / or of the double rotary frequency 2*fn.
If you have a radial misalignment you get two shocks / round in different directions  that means 2fn!
If you have an angular misalignment . Both shocks are going in the same direction  1fn!!

## Slide 4
Double cardanic couplings
Double cardanic couplings are usually used to: - allow higher misalignment
- reduce restoring force
- increase distance between shaft end

## Slide 5
Double cardanic spacer coupling: ROTEX® ZS-DKM
Current Standard
State of the art
Single cardanic spacer coupling:
Double cardanic coupling – reduced restoring force
radial forces create bending forces
radial misalignment is transformed
to angular misalignment.
ΔKrad
ΔKrad
ΔKW
In a double cardanic coupling like ROTEX ZS-DKM the spacer will be in a smooth line between the coupling hubs. The radial forces are reduced to a minimum.

## Slide 6
Double cardanic elastic couplings

## Slide 7
ROTEX® ZS-DKM-H
The ROTEX® ZS-DKM-H is developed mainly for the pump industry. The main innovation is the simplified mounting and dismounting. Only 4 screws need to be tightened.
The ROTEX ZS-DKM-H is ideal for transmitting torque while damping torsionnal vibrations and absorbing shocks produced by uneven operation
The half hubs will be fixed in the right position by the bolts (position 1).
high misalignment ability (double cardanic system)
the radial forces to be reduced to a minimum
vibration and noise reduction
the adjustment between motor and pump shaft is very simple; in some cases not necessary
many different elastic damping rings available
Double cardanic Rotex ZS-DKM H

## Slide 8
Double cardanic Rotex ZS-DKM H – Elastic spiders
ROTEX®-GS
ROTEX®-Standard
The GS spider has a straight tooth and is pre-stressed. That makes sure that the spacer is well supported.
The Standard spider has curved tooth for standard applications without spacer.
The central web supports the spacer in radial direction! This ensures, that the spacer remains in his position if the tooth are worn out!
Limitation by a concave cams in case of to high speeds/centrifugal forces.

## Slide 9
ROTEX ZS-DKM-H
Radial misalignment
If the drive isn’t aligned the ROTEX ZS-DKM-H creates a vibration signature.
This is explained by the spacer centered by the GS type spider
This enables a condition diagnose about the alignment with the on- or offline monitoring.
The test was drive under nominal Torque with max. misalignment!
The higher the misalignment the bigger the vibration signature – The shown signature is at the max rad. misalignment!
The signature is basically not dependant of the wear of the coupling!
Double cardanic Rotex ZS-DKM H – vibration signature

## Slide 10
Alignment in cold condition
Alignment after a few minutes
Alignment after heating up
ROTEX® ZS-DKM-H–temperature influence & misalignment

## Slide 11
ROTEX® ZS-DKM-H–temperature influence & misalignment
ROTEX® 75 ZS-DKM-H
max. radial misalignment: 2,19mm
ROTEX® 75 A-H single cardanic
max. radial misalignment: 0,48 mm
PolyNorm® 90 AZR single cardanic
Max. rad. misaligment: 0,35 mm
h1
Radial misalignment in relation to the fluid temperature
Dimension h1 [mm]
Radial misalignment ΔKR [mm]

## Slide 12
Heating up
Acceleration / time signal Aeff [m2/s]
Temperature [°C]
Time
The growth of the Pump housing between room temperature and 350°C
Was 1.3mm!! The Pump drive was warm aligned.
The vibration coursed by the misalignment in the cold condition was very high.
After heating up the vibrations were reduced to a lower level.
That’s the normal way! ..But which coupling can handle 1.3mm radial
misalignment?! ….Only the ROTEX ZS-DKM-H!!
ROTEX® ZS-DKM-H–temperature influence & misalignment

## Slide 13
Double cardanic rigid couplings
Notes: 13

## Slide 14
RIGIFLEX®-N A
API 610/671
coupling flange
coupling flange
puller holes
centering
The spacer will be removable within the steel laminae and the adapter flanges. If the screws are in the puller holes, the adapter flanges will move against the hollow shaft of the spacer. The adapter flanges will leave the centering and the spacer could be removed in radial direction.

## Slide 15
RIGIFLEX®-N A
API 610/671
safety device
coupling hub
bolt
lamina packing
hollow shaft
.
The spacer is centered through the bolts

## Slide 16
RIGIFLEX®-N
Steel laminas couplings are creating no vibrations!
No vibration difference due to misalignment could be measured.
The spacer is centered through the bolt
Both test were made with completely destroyed laminas.
Vibration level : independent of the wear in laminas:
Condition monitoring
Picture 1: drive under torque without misalignment
Picture 2 : drive under torque with max. misalignment!

## Slide 17
Vibrations and mechanical couplings